# STM8 template “ADC2_measure“

### Functional Description:
measure GPIO voltage via ADC2 and send result to PC via UART1. Also blink LED periodically

Details:
- change CPU clock prescaler
- initialize ADC2 for single shot mode
- initialize UART1 for 115.2kBaud
- measure voltage on PB5 and send via UART1
- control LED
- pause execution via timer 3
- no interrupts
### Hardware Requirements:
- Compatible with muBoard (custom)
- Analog signal (0..Vcc) connected to pin PB5 (=AIN5)
- UART1 pins PA4/Rx and PA5/Tx connected to PC via USB or RS232
- LED connected to PD0

### Used STM8Lib Modules (see Makefile):
gpio, timer3, uart1, adc2, putchar

### Notes:
Advanced ADC1 features like analog watchdog etc. are not implemented